## Slide 1: Air Quality Forecast Challenge
V. Gillioz, C. Sicard, K. Pyszkowski
17.05.2021

## Slide 2: Agenda
Data Pipeline
Data Visualization
Data Preprocessing
Forecasting PM2.5 Time Series Using a Recurrent Neural Network
Comparison of Our Model with Other Time-Series Forecasting Methods
  Data Prediction using Fast Fourier Transform
  Data Prediction using Facebook Prophet
  Data Prediction using SARIMA
Conclusion

## Slide 3: 1. Data Pipeline

## Slide 4: Setup of Data Pipeline
Measurements by SPS30 and DHT22 sensors on a Raspberry Pi
Python interface for analysis and visualization
Thingspeak IoT
Every 5 minutes :
  1 measurement is made
  Saved on Raspberry Pi in CSV format
  Uploaded on Thingspeak IoT
But it after 6 days it stopped working…

## Slide 5: Issues with the Initial Data Pipeline
Only 6 days of measurements, so ~1’500 measurements
Get a new Raspberry ? Not enough time
Use public data
  National Air Pollution Monitoring Network
    1 measurement every hour
    In a few big cities of Switzerland
First strategy : Get the same amount of data samples from NABEL so that we have the initially planned number of collected data
  Bad strategy  Not the same time intervals (5 minutes vs. 1 hour)

## Slide 6: 2. Data Visualization

## Slide 7: Dataset Visualization

## Slide 8
Temperature (in °C)
Precipitation (in mm)
PM2.5 (in µg/m3)
PM10 (in µg/m3)
Correlogram of the dataset and its variables
Variables Visualization
We first merged our two sources of data
But not great since the time intervals between two measurements are different
There are also a lot of missing values
Missing values

## Slide 9: 3. Data Preprocessing

## Slide 10: Imputation of Large Missing Data Intervals
Dynamic Time Warping (DTW) had bad results in finding similarities between the two curves
However, the high correlation (0.93) between PM10 and PM2.5 indicates strong similitudes between the two variables
We interpolated the larges missing gaps linearly, by multiplying PM2.5 by the average of PM10/PM2.5
It increased the correlation by a small value, but we consider it still coherent (0.95)

## Slide 11: Removal of Outliers
Outliers are detected using Standard Deviation on a sliding window
If the Absolute Deviation of the sample divided by the Standard Deviation of the interval is above a chosen threshold, the outlier is removed and then linearly interpolated
This method has given good results, but may be slightly improved by using the median instead of the mean because it is less influenced by the outliers

## Slide 12: Rescaling the Raspberry Pi Data Using the NABEL Mean
In order to create coherence between our measured data and the NABEL data, we rescale the Raspberry Pi measures with respect to the NABEL data, which corresponds to means on a 1-hour interval

## Slide 13: Adding Raspberry Pi Noise to the NABEL Data
We compute the variation of the rescaled Raspberry Pi noise around the NABEL Data
The variation at each point is divided by the NABEL value at this point to compute a proportional deviation
This proportional deviation takes the form of a Multivariate Gaussian Distribution, with PM10 and PM2.5 noise being strongly correlated
We then added random noise with the same distribution to the NABEL Data for which we did not have corresponding Raspberry Pi Data
The correlation between PM10 and PM2.5 after noising is 0.92, very close to our original correlation of 0.93

## Slide 14: Imputed Dataset Visualization

## Slide 15
Temperature (in °C)
Precipitation (in mm)
PM2.5 (in µg/m3)
PM10 (in µg/m3)
Correlogram of the imputed dataset and its variables
Imputed Dataset Visualization

## Slide 16
Temperature (in °C)
Precipitation (in mm)
PM2.5 (in µg/m3)
PM10 (in µg/m3)
Comparison with the Non-Preprocessed Dataset
Temperature (in °C)
Precipitation (in mm)
PM2.5 (in µg/m3)
PM10 (in µg/m3)

## Slide 17: 4. Forecasting PM2.5 Time-Series Using a Recurrent Neural Network (RNN)

## Slide 18: Reducing the Dataset
Our data after the pre-processing represents only ~2% of the dataset
As only ~1’600 of the data comes from our measurements, we wanted it to be included in both validation and testing of our dataset
For this purpose, we decided to take only the last 10’000 data samples to get the train-validation-test split of our data
Train set
Validation set
Test set
We divided the reduced dataset as follows : 70% for training, 10% for validation and 20% for testing

## Slide 19: Long Short-Term Memory (LSTM)
Error metric :
  Note: This error metric cannot use actual values equal to 0
  To prevent this, we decided to add 1 to each value, turning into this formula instead:
Best number of epochs : 10
Best number of neurons in the input layer : 200
MAPE (in %) |  | Number of neurons in the input layer |  |  |  |  |  |  | 
 |  | 1 | 2 | 10 | 25 | 50 | 100 | 150 | 200
Number of iterations (epochs) | 1 | 51.43 | 46.65 | 72.70 | 81.14 | 82.53 | 68.70 | 58.91 | 57.50
 | 2 | 81.67 | 70.60 | 83.88 | 76.09 | 61.83 | 53.43 | 47.08 | 43.84
 | 10 | 86.17 | 63.66 | 42.62 | 40.41 | 38.26 | 35.50 | 35.02 | 33.79
 | 25 | 49.33 | 38.32 | 39.41 | 38.17 | 36.30 | 36.10 | 35.22 | 35.08
 | 50 | 37.75 | 38.69 | 38.50 | 36.84 | 35.68 | 35.64 | 35.59 | 35.36
 | 100 | 36.71 | 36.31 | 35.77 | 35.32 | 35.41 | 35.43 | 35.45 | 35.69
 | 150 | 36.67 | 35.23 | 36.48 | 35.64 | 35.52 | 35.65 | 35.81 | 35.86
 | 200 | 35.56 | 35.60 | 34.41 | 35.27 | 35.17 | 35.39 | 35.64 | 35.73

## Slide 20: Best Tested Parameters for RNN-LSTM
Number of epochs : 10
Number of neurons in the input layer : 200
Error percentage :
The prediction is performed on the test set after the model has been trained using training and validation sets

## Slide 21: 5. Comparison of Our Model with Other Time-Series Forecasting Methods
a. Data Prediction using Fast Fourier Transform

## Slide 22: Data Prediction with FFT
Best Validation Loss - 58.74
Test Loss - 91.37
We ran a cross-validation to find the optimal split between training and validation sets and the best "blurring" parameter, with MAPE Loss to compare it with the other models we trained

## Slide 23: 5. Comparison of Our Model with Other Time-Series Forecasting Methods
b. Data Prediction using Facebook Prophet

## Slide 24: Data Prediction with Facebook Prophet
Time series are decomposed with the following equation:
represents the trend function
the seasonality
potential holidays (irregular patterns that can occur over a period of time).
The Facebook Prophet model is for forecasting time series data based on an additive model where non-linear trends are fit with seasonality.

## Slide 25: 5. Comparison of Our Model with Other Time-Series Forecasting Methods
c. Data Prediction using SARIMAX

## Slide 26: Best Tested Parameters for SARIMA
Order:
Seasonality order :
Error percentage :
The prediction is performed on the test set (100 samples) after the model has been fitted on 900 previous values.

## Slide 27: 6. Conclusion

## Slide 28: Conclusion
The data must be gathered and used carefully
The quality of the data has a lot of influence on the quality of the models
Bad data  (likely) bad results with a good model
Measured data can be quite different from the reality, due to among others:
  Cheap hardware, which might give not very precise measurement
  Sensors are put in places that are not 100% representative of the overall weather conditions (too exposed to the sun, too exposed to humidity…)
Error was never below 34% for LSTM, which is still quite good but not totally reliable
100% accuracy is not possible when predicting air quality

## Slide 29: One Last Example

## Slide 30: End of the World on May 4th
(Wrongly) Training models can lead to surprising results…

## Slide 31: References
J. Brownlee, Multivariate Time Series Forecasting with LSTMs with Keras, Machine Learning Mystery, 2017 (link)
S. J. Taylor, B. Letham, Forecasting at Scale, Facebook Open Source, (link) (paper)
R. C. Staudemeyer, E. Rothstein Morris, Understanding LSTM -- a tutorial into Long Short-Term Memory Recurrent Neural Networks, 2019 (link)

## Slide 32: Thank you for your attention!
And a special thank you to Sachit whose help dealing with the Raspberry issues was really appreciated and useful